## Slide 1: Portable biometrics for determining cognitive load from galvanic skin response
Guido Zuidhof
December 2014

## Slide 2: Cognitive load measurement
Many approaches to measuring cognitive load
R. Brünken et al. (2003), Direct Measurement of Cognitive Load in Multimedia Learning. Educational Psychologist 38(1), 53-61
 | Indirect | Direct
Subjective | Self-reported invested mental effort | Self-reported stress level Self-reported difficulty of materials
Objective | Psysiological measures Learning outcome measures | Brain activity measures (e.g. fMRI) Dual-task performance

## Slide 3: Cognitive load measurement
In my thesis we are focusing on psychological measures
 | Indirect | Direct
Subjective | Self-reported invested mental effort | Self-reported stress level Self-reported difficulty of materials
Objective | Psysiological measures Learning outcome measures | Brain activity measures (e.g. fMRI) Dual-task performance

## Slide 4: Psychiological response
The body displays a response under an increased cognitive load
Many different options for measuring

## Slide 5: Heart rate variability (HRV)
Time between heart beats

## Slide 6: Galvanic Skin Response (GSR)
Or Electrodermal Response (EDR), Skin Conductance Response (SCR)
Measuring the electrical conductance of skin
Gets influenced by sweat and openness pores

## Slide 7: Respiratory rate
Or Ventilatory rate, Breathing frequency

## Slide 8: Other psysiological responses
Blood oxygen level
Skin temperature / heat flux
Blood pressure
Motion (measured using accelerometer)
...
One generally does not exclude the others

## Slide 9: New smartwatches feature biometric sensors
Samsung Simband
Microsoft Band
BASIS Watch
APIs are generally lacking, data is locked in proprietary apps

## Slide 10: Why measure cognitive load?
“You should take a break”
Automatic difficulty adjustment in applications (such as games)
People on the autism spectrum do display psychiological response, this can be used to predict ‘explosions’ of emotions
Classroom applications, are students following/getting it?

## Slide 11: GSR
I decided measure the galvanic skin response,
Classify task difficulty from features of the GSR data

## Slide 12: Experiment

## Slide 13: Apparatus
Affectiva Q Sensor (dry electrodes on wrist)
BIOPAC MP30
(wet finger electrodes)

## Slide 14: Raw data

## Slide 15: Raw data
DC current noise (50Hz) in signal

## Slide 16: Preprocessing
Smoothing filter (removing DC current)
(Savitzky-Golay filtering)

## Slide 17: Preprocessing
Cutting the tasks out of the data
...

## Slide 18: Final preprocessing
Normalizing (dividing by subject average GSR over all tasks)
Smoothing out small DC current spikes (Savitzky-Golay filtering)

## Slide 19: Transformation
Extract time and frequency domain information
Export to WEKA readable format (CSV)
'luc' 'diff1' [220.5357] [0.1225]
(Name, Difficulty, accumulative GSR, Average GSR)