## Slide 1: Using GSR data for determining cognitive load
Guido Zuidhof
December 2014

## Slide 2: Cognitive Load
The amount of information a human is trying to process in working memory at any one time.
(Sweller, 1999)

## Slide 3: Why determine cognitive load?
Classroom applications
Automatic difficulty adjustment in applications (such as games)
“You should take a break”
People on the autism spectrum do display physiological response
Notes: People with autism find it hard to become aware / communicate cognitive load

## Slide 4: Cognitive load measurement
Many approaches to measuring cognitive load
R. Brünken et al. (2003), Direct Measurement of Cognitive Load in Multimedia Learning. Educational Psychologist 38(1), 53-61
 | Indirect | Direct
Subjective | Self-reported invested mental effort | Self-reported stress level Self-reported difficulty of materials
Objective | Physiological measures Behavioral measures Learning outcome measures | Dual-task performance Brain activity measures (e.g. fMRI) (arguably also indirect)

## Slide 5: Cognitive load measurement
Many approaches to measuring cognitive load
 | Indirect | Direct
Subjective | Self-reported invested mental effort | Self-reported stress level Self-reported difficulty of materials
Objective | Physiological measures Behavioral measures Learning outcome measures | Dual-task performance Brain activity measures (e.g. fMRI) (arguably also indirect)

## Slide 6: New consumer electronics can measure biometrics
Samsung Simband
Microsoft Band
BASIS Watch
APIs are generally lacking, data is locked in proprietary apps

## Slide 7: Physiological response
The body responds when cognitive load is increased/reduced
Many different options for measuring, like:
Blood oxygen level
Skin temperature / heat flux
Blood pressure
Motion (accelerometer)
Heart rate variability
Respiratory rate
Galvanic Skin Response
Facial expressions
Pupil dilation
Measuring these is often not mutually exclusive
Notes: Multiple can be measured simultaneously

## Slide 8: Physiological response
The body responds when cognitive load is increased/reduced
Many different options for measuring, like:
Blood oxygen level
Skin temperature / heat flux
Blood pressure
Motion (accelerometer)
Heart rate variability
Respiratory rate
Galvanic Skin Response (GSR)
Facial expressions
Pupil dilation

## Slide 9: Galvanic Skin Response (GSR)
Measuring the electrical skin conductance
Small voltage applied to electrodes, flowing current measured
Unit of measurement: μS (microsiemens)
Influenced by sweat glands
Delay between stimulus and response between 0.8 and 4 seconds
Notes: GSR is measuring the electrical skin conductance,
Unit of measurement is micro siemens
More sweat -> higher conductance, sweating caused by primitive ‘fight or flight’ response, preparing for exertion to deal with threat
Delayed response

## Slide 10: Goal
Determining cognitive load from GSR data
Method
Measure GSR data using tasks with varying difficulty
Classify task difficulty from features of the GSR data

## Slide 11: Experiment
Arithmetic tasks with varying difficulty
Addition of four numbers, presented one by one
4 difficulty levels
8 tasks per subject, in random order
Difficulty | Example Task
1 | 0 + 1 + 1 + 1
2 | 3 + 5 + 7 + 2
3 | 31 + 40 + 67 + 24
4 | 163 + 721 + 573 + 594

## Slide 12
***

## Slide 13
48

## Slide 14
71

## Slide 15
50

## Slide 16
34

## Slide 17
203
196
199

## Slide 18
**

## Slide 19: Apparatus
Affectiva Q Sensor (dry electrodes on wrist)
BIOPAC MP30
(wet finger electrodes)

## Slide 20: Q Sensor Data
Data proved unusable, proper connection to skin not present in many subjects
Needs some sweat present from the get-go
Lesson learned:
  Have subjects wear them longer before the first task starts
  Ask subjects to do some mild exercise beforehand

## Slide 21: Raw data

## Slide 22: Raw data
DC current noise (50Hz) in signal

## Slide 23: Preprocessing
Smoothing filter (removing DC current)
(Savitzky-Golay filtering)
Notes: Low Pass Filter didn´t cut it

## Slide 24: Preprocessing
Cutting the tasks out of the data
...

## Slide 25: Final preprocessing
Normalizing (dividing by subject average GSR over all tasks)
Smoothing out small DC current spikes (Savitzky-Golay filtering)

## Slide 26: Transformation
Extract time domain features
Export to an easily parsable format (CSV)
Subject, Difficulty,
Accumulative GSR, Average GSR
Standard Deviation, Difference start/end
Peak count with varying tresholds
'luc' 'diff2' [221.4503] [0.1230] [7.3118e-04] [0.0020] [6] [6] [5] [4]

## Slide 27: Visualization
Average GSR

## Slide 28: Visualization
Average GSR

## Slide 29: Visualization
Standard Deviation

## Slide 30: Visualization
Standard Deviation

## Slide 31: Building a classifier
CSV data fed to Weka Data Mining Software
Easy to try multiple classifier training algorithms

## Slide 32: Classification
Can we predict the task difficulty given these features?

## Slide 33: Preliminary results
Simple classifiers seem to work best. Expected from small dataset size.
Classifier | Correctly Classified Instances %
SimpleCart (Minimal Cost Decision Tree) | 33.33%
J48Graft (Decision tree) | 43.75%
BayesNet (Bayesian probability estimation) | 25%
Naïve Bayes | 33.33%
LWL (Locally weighted learning) | 41.67%
Multilayer Perceptron (20 hidden layers) | 29.17%
SMO (Support Vector Machine class algorithm) | 6.25%
JRIP (Rule based learner) | 18.75%
10 Folds cross-validation was used
Notes: Note that 25% is expected from chance
Not great.

## Slide 34: Preliminary results
Classifier | Correct % 4 classes | Correct % 2 classes
SimpleCart (Minimal Cost Decision Tree) | 33.33% | 72.92%
J48Graft (Decision tree) | 43.75% | 77.08%
BayesNet (Bayesian probability estimation) | 25% | 75%
Naïve Bayes | 33.33% | 60.42%
LWL (Locally weighted learning) | 41.67% | 75%
Multilayer Perceptron (20 hidden layers) | 29.17% | 62.50%
SMO (Support Vector Machine class algorithm) | 6.25% | 58.33%
JRIP (Rule based learner) | 18.75% | 79.12%
10 Folds cross-validation was used
Notes: Classifying between task 1,2 and task 3,4 combined
50% expected from chance.
Still not great / good enough

## Slide 35: Improving the classification
Classification accuracy is not great however, possible reasons
Small dataset (6 participants * 8 tasks = 48 entries)
Experiment
  Design susceptible to ´task bleeding´, i.e. sweat from last task carries over
  Sensor inaccuracy
Not the right features extracted from data
It is simply not classifiable better from GSR data

## Slide 36: Recap
Using biometrics to determine cognitive load outside of the lab is exciting and potentially useful
I measured GSR during tasks of varying difficulty
Classifying task difficulty from this data is the goal
Next up is seeing whether I can improve this classification by extracting different features