## Slide 1: Smart watch and Biopac: using GSR data for distinguishing cognitive states
Guido Zuidhof
December 2014

## Slide 2: Cognitive load measurement
Many approaches to measuring cognitive load
R. Brünken et al. (2003), Direct Measurement of Cognitive Load in Multimedia Learning. Educational Psychologist 38(1), 53-61
 | Indirect | Direct
Subjective | Self-reported invested mental effort | Self-reported stress level Self-reported difficulty of materials
Objective | Physiological measures Behavioral measures Learning outcome measures | Dual-task performance Brain activity measures (e.g. fMRI) (arguably also indirect)

## Slide 3: Cognitive load measurement
Many approaches to measuring cognitive load
 | Indirect | Direct
Subjective | Self-reported invested mental effort | Self-reported stress level Self-reported difficulty of materials
Objective | Physiological measures Behavioral measures Learning outcome measures | Dual-task performance Brain activity measures (e.g. fMRI) (arguably also indirect)

## Slide 4: New smartwatches feature biometric sensors (measuring physiological signals)
Samsung Simband
Microsoft Band
BASIS Watch
APIs are generally lacking, data is locked in proprietary apps

## Slide 5: Physiological response
The body responds when cognitive load is increased/reduced
Many different options for measuring, like:
Blood oxygen level
Skin temperature / heat flux
Blood pressure
Motion (accelerometer)
Heart rate variability
Respiratory rate
Galvanic Skin Response
Facial expressions
Pupil dilation
Measuring these is often not mutually exclusive
Notes: Multiple can be measured simultaneously

## Slide 6: Physiological response
The body responds when cognitive load is increased/reduced
Many different options for measuring, like:
Blood oxygen level
Skin temperature / heat flux
Blood pressure
Motion (accelerometer)
Heart rate variability
Respiratory rate
Galvanic Skin Response (GSR)
Facial expressions
Pupil dilation

## Slide 7: Galvanic Skin Response (GSR)
Measuring the electrical skin conductance
Small voltage applied to electrodes, flowing current measured
Unit of measurement: μS (microsiemens)
Influenced by sweat glands
Delay between stimulus and response between 0.8 and 4 seconds
Notes: GSR is measuring the electrical skin conductance,
Unit of measurement is micro siemens
More sweat -> higher conductance, sweating caused by primitive ‘fight or flight’ response, preparing for exertion to deal with threat
Delayed response

## Slide 8: Why measure cognitive load?
“You should take a break”
Automatic difficulty adjustment in applications (such as games)
People on the autism spectrum do display physiological response
Classroom applications, are students following/getting it?

## Slide 9: Goal
Determining cognitive load from GSR data
Method
Measure GSR data using tasks with varying difficulty
Classify task difficulty from features of the GSR data

## Slide 10: Experiment
Arithmetic tasks with varying difficulty
Addition of four numbers, presented one by one
4 difficulty levels
8 tasks per subject, in random order
Difficulty | Example Task
1 | 0 + 1 + 1 + 1
2 | 3 + 5 + 7 + 2
3 | 31 + 40 + 67 + 24
4 | 163 + 721 + 573 + 594

## Slide 11
***

## Slide 12
48

## Slide 13
71

## Slide 14
50

## Slide 15
34

## Slide 16
203
196
199

## Slide 17
**

## Slide 18: Apparatus
Affectiva Q Sensor (dry electrodes on wrist)
BIOPAC MP30
(wet finger electrodes)

## Slide 19: Raw data

## Slide 20: Raw data
DC current noise (50Hz) in signal

## Slide 21: Preprocessing
Smoothing filter (removing DC current)
(Savitzky-Golay filtering)
Notes: Low Pass Filter didn´t cut it

## Slide 22: Preprocessing
Cutting the tasks out of the data
...

## Slide 23: Final preprocessing
Normalizing (dividing by subject average GSR over all tasks)
Smoothing out small DC current spikes (Savitzky-Golay filtering)

## Slide 24: Transformation
Extract time domain features
Export to an easily parsable format (CSV)
(Subject, Difficulty, Accumulative, Average, Standard Deviation, Peak count with varying tresholds)
'luc' 'diff2' [221.4503] [0.1230] [7.3118e-04] [0.0020] [6] [6] [5] [4]
luc,diff2,221.4503,0.12303,0.00073118,0.0019555,6,6,5,4

## Slide 25: Building a classifier
CSV data fed to Weka Data Mining Software
Easy to try multiple classifier training algorithms
Also great for visualization

## Slide 26: Visualization
Average GSR

## Slide 27: Visualization
Average GSR

## Slide 28: Visualization
Standard Deviation

## Slide 29: Visualization
Standard Deviation

## Slide 30: Preliminary results
Simple classifiers seem to work best. Expected from small dataset size.
Classifier | Correctly Classified Instances %
SimpleCart (Minimal Cost Decision Tree) | 33.33%
J48Graft (Decision tree) | 43.75%
BayesNet (Bayesian probability estimation) | 25%
Naïve Bayes | 33.33%
LWL (Locally weighted learning) | 41.67%
Multilayer Perceptron (20 hidden layers) | 29.17%
SMO (Support Vector Machine class algorithm) | 6.25%
JRIP (Rule based learner) | 18.75%
10 Folds cross-validation was used
Notes: Note that 25% is expected from chance
Not great.

## Slide 31: Preliminary results
Classifier | Correct % 4 classes | Correct % 2 classes
SimpleCart (Minimal Cost Decision Tree) | 33.33% | 72.92%
J48Graft (Decision tree) | 43.75% | 77.08%
BayesNet (Bayesian probability estimation) | 25% | 75%
Naïve Bayes | 33.33% | 60.42%
LWL (Locally weighted learning) | 41.67% | 75%
Multilayer Perceptron (20 hidden layers) | 29.17% | 62.50%
SMO (Support Vector Machine class algorithm) | 6.25% | 58.33%
JRIP (Rule based learner) | 18.75% | 79.12%
10 Folds cross-validation was used
Notes: Classifying between task 1,2 and task 3,4 combined
50% expected from chance.
Still not great / good enough

## Slide 32: Improving the classification
Classification accuracy is not great however, possible reasons
Small dataset (6 participants * 8 tasks = 48 entries)
Experiment
  Design susceptible to ´task bleeding´, i.e. sweat from last task carries over
  Sensor inaccuracy
Not the right features extracted from data
It is simply not classifiable better from GSR data

## Slide 33: Summary
Using biometrics to determine cognitive load outside of the lab is exciting
I measured GSR during tasks of varying difficulty
Classifying task difficulty from this data is the goal
Next up is seeing whether I can improve this classification